Document Description and Purpose

Following is a description of the ALI Record fields relevant to Phase I & Phase II wireless service.  The requirements set forth in this document constitute the “standards” established for all Phase I & II ALI Records in the State of Arizona.  Covered is 
1) content, i.e., what verbiage is to be used in particular fields, and 2) positioning, i.e., which field will be used to populate the content.

It is the intent of the State of Arizona’s 9-1-1 Office to provision each PSAP with Qwest’s 30W ALI data stream before the turn-up of Phase I or Phase II service.  Therefore, these standards have developed around the 30W format.

These standards are intended for the use of Arizona’s public safety community; the wireless service providers (WSP); as well as, the 9-1-1 database providers.

Finally, these standards have been developed during a period when no national standards are in place.  Should national standards be developed and approved, Arizona’s 9-1-1 Office will evaluate those standards and make modifications to AZ’s standards as deemed appropriate.

Positioning of Data

In order to be ready for the future XML wireless format, AZ’s standards call for parsing of data, or populating fields with their respective content.

Example:	123 ½ E Main St Omni

Correct Positioning:

House Number Field:	123

House Number Suffix Field	½

Prefix Directional Field:	E

Street Name Field 1:	Main St Omni*

Incorrect Positioning:

Street Name Field 1:	123 ½ E Main St Omni

*	Note:  Qwest’s 30W ALI data stream does not contain a unique or discretionary field for the direction of the tower sector.  Therefore, that information should follow the name of the street in the Street Name 1 field.

Capitalization & Punctuation

Capitalization and punctuation shall be used in the following ways:

Capitalization

Acronyms and initialisms (acronyms that are not pronounceable) should be all capitals.  Example:

AZ	(Arizona)

PCS	(Personal Communications Service)

WRLS	(Wireless)

Abbreviations – The first letter of an abbreviation should be capitalized, followed by lower case letters.  Example:

Ave	(Avenue)

Blvd	(Boulevard)

E	(East)

Hwy	(Highway)

St	(Street)

Punctuation

Although correct English calls for “periods” after abbreviations, they will not be used on the ALI Records.  Example:

Ave	(Avenue)

NE	(North East)

PD	(Police Department)

SO	(Sheriff’s Office)

Note:   Intrado can use caps and lower case as defined above with NCAS solutions.  However, the ALI Records of those carriers using the WID solution can only be all caps.

Note:  The customer name field is delivered from Intrado’s ALI system (it is part of the shell record).  This system can only deliver all caps.  Therefore, all carriers who are Intrado clients will have their name formatted with all caps (rather than the way the standards designate).

30W ALI Data Stream Fields

Below are the fields in the 30W ALI data stream that the 9-1-1 system’s Wireless Administrator should have input regarding how they are populated.

Customer Name Field

House Number Field

House Number Suffix Field

Prefix Directional Field

Street Name Field 1

Street Name Field 2

State Field

City Field (a.k.a. Community Field)

Locality Field (a.k.a. PSAP= Field)

Police Field (ELT section)

Fire Field (ELT section)

Meds Field (ELT section)

Customer Name Field

This field will be populated with the name of the wireless service provider (WSP).  If the carrier in question provides wire line and wireless service, then the name should designate that this is the carrier’s wireless service.

Example:	Sprint PCS	(not just Sprint)

Additionally, following the customer name, the 24x7 telephone number for the provider’s security division should also appear.  If the provider does not have a security number, then the repair number will be shown instead.

Example:	Verizon WRLS _ _ _-_ _ _ -_ _ _ _ (10-digit telephone number)

How each carrier’s name and number should appear is found further on in this document in the section titled “Wireless Service Providers Name Standards”.

Note:  Due to a limited amount of characters allowed in the Customer Name Field (there are 28), abbreviations may be necessary.

Responsible Party:

The wireless service provider and/or their database vendor, is responsible to ensure that their name, and 24x7 security number, is displayed as described here and in the final section of this document.

It is also the responsibility of the wireless service provider to notify the State of Arizona’s 9-1-1 Office at 602-771-0911 if their name or security number changes.  This notification will need to be followed by the WSP, and/or their representative, altering the file that contains the information in the “Customer Name” field.

Fields Associated with the Cell Site Street Address

Following are the fields that may be used to identify the cell site address.

(	House Number Field

(	House Number Suffix Field

(	Prefix Directional Field

(	Street Name Field 1

(	Street Name Field 2

These fields will be used to identify the location of the cell site that is generating the 
9-1-1 call.  That site will be identified in one of the following ways:

(	MSAG valid, legal street address (preferable)

(	Intersection

(	Descriptor (ex: .Pike’s Peak, Mummy Mountain)

Regardless of whether the location is identified by a legal street address, intersection, or descriptor, the information should be followed by a description of the cell sector’s coverage area.  Specifically:

If the cellular tower:

(	Has only one sector, then the word “Omni” shall follow the street name.

Example:	Mummy Mountain Omni

(	Has 2 or more sectors, then the direction of that sector shall follow the street name.

Example:	123 E Main St NW

Example:	I10 – Camelback Rd E

Note:  Street Name Field 2 has no specific use, other than to be used (as necessary) for the continuation of the address in Street Name Field 1.  If it is not needed for the continuation of the address, this field can be used to further describe the address or cell site/sector.  It is important to note, however, that although Street Name Field 2 is part of Qwest’s 30W ALI data stream, not all database providers have it provisioned, and in turn, display it.  Therefore, discussion with the database provider is necessary before requesting that information be placed in this field.

Responsible Party:

The 9-1-1 Wireless Administrator is responsible to advise the WSP, and/or their database representative, how this field should be populated.  The Wireless Administrator is also responsible to ensure that the street name entry is MSAG valid.

The WSP, and/or their representative, is responsible to ensure that the ALI Record is populated as advised.

City Field  (a.k.a. Community Field)

Like the Company ID field, this is a field that is necessary in order to generate Qwest’s Wireless Metrics Report.  It must be formatted in a very specific way.

The first eleven characters (9 numbers and 2 dashes) of the field are to identify the particular cell site, cell sector, and Switch ID.  These 3 components will be separated by a “dash” (-) and be sequenced in the order described above.  The eleven characters will be followed by a “comma” (,), “blank space”, then the community name related to the cell site address.

Example:	00103-1-001, Scottsdale

00103 = cell site

1 = cell sector

001 = switch ID

In most cases, the cell sector should be represented in the following way.

0 = Omni

1 = Alpha

2 = Beta

3 = Gamma

In some instances, a wireless carrier will use “4” as a sector ID.  When this occurs, “4” should be populated in the community field in the “cell sector” location.  When these sectors are used:

Example:	00103-4-001, Scottsdale

Also, Cingular uses 7,8,9 in place of 1,2,3 when the sector uses their UMTS air interface.  These should also be represented in the “cell sector” location.

7 = Alpha

8 = Beta

9 = Gamma

Example:	00103-8-001, Scottsdale

Note:  Some naming schemes do not use 0 through 3 to represent cell sectors.  Rather, they use X, Y, Z or A, B, C.  These alternate representations (letters) are not permitted.

Note:  The Switch ID should not be confused with the MSC ID.  The MSC is the Mobile Switching Center.  Within the MSC (center) resides many actual switches.  The MSC number (MSC ID) is the "center" the call came into and the Switch number (Switch ID) is the actual box that switches the 911 calls from the tower down the trunks to the Selective Router.  The MSC ID is 5-digits, where the Switch ID is 3.

Note:  Some 9-1-1 wireless systems may find that they have the same Switch ID for different WSPs.  This is permissible.  On the surface it may seem that this would prevent the correct gathering of data for the Qwest Metrics report.  However, this is not the case since the data collection process also considers the Company ID.

Note:  GSM technology does not use a switch ID.  Therefore, in those instances that a carrier is using GSM, the switch ID should be represented as 000.

Note:  There are a few instances where the carrier uses a numeric/alpha combination to represent the sector.  For the purposes of the standards, we will not include the alpha character (only the numeric) in the community field.

Responsible Party:

The WSP, and/or their representative, will provide the 9-1-1 Wireless Administrator information to assist in the development of the cell site, cell sector, Switch ID section of this field.  The Wireless Administrator will consider that information in the formation of this field, with the final call regarding how this field will be populated falling to the Administrator.

The WSP, and/or their representative, is responsible to ensure that the ALI Record is populated as advised.

State Field

This field shall be populated with “AZ”.

Responsible Party:

It should be understood that AZ will be populated in this field.  In those rare instances, however, where the cell site address falls in an adjoining state, it is the 9-1-1 Wireless Administrator’s responsibility to identify and pass the state abbreviation to the WSP, and/or their representative.

The WSP, and/or their representative, is responsible to ensure that the ALI Record is populated as advised.

Class of Service Field

In Arizona, the class of service (COS) standards are as follows:

COS	Application

CELL	Not used in Arizona.

MOBL	Phase 0.5

WRLS	Phase 1

WPH1	Phase II, the calling party’s X/Y coordinates cannot be sent.  Instead, the coordinates of the cell site are received.

WPH2	Phase II, the calling party’s X/Y coordinates are sent.

Responsible Party:

The wireless service provider will manage this field via the “External Security/MPC Cross Table Update Form

Company ID Field

Because this field is necessary to correctly collect and report data on Qwest’s Wireless Metrics Report, the State of Arizona considers this a required field.  This field must be populated with each wireless service provider’s unique Company ID (a.k.a., NENA ID).

Responsible Party:

The wireless service provider is responsible to secure a company ID and ensure that it is embedded in the ALI data stream.

Location Field

In an NCAS solution the location field will carry the calling party’s ten-digit call back number.  The call back number should be proceeded with “CALLBK = ”.

Note: this rule does not apply to WID (Wireless Integration Device) solutions.

Responsible Party:

The wireless service provider will manage this field via the “External Security/MPC Cross Table Update Form”.

ELT (English Language Translations) Field

The ELTs are established per wireless ESN.  They shall read:

Police:	Verify police

Fire:	Verify fire

Meds:	Verify meds

Responsible Party:

The MSAG Coordinator is responsible to pass the ELTs (as defined above) to Intrado when they secure the wireless ESN(s).

Locality Field

The Locality Field is established per wireless ESN.

The Locality Field is displayed just above the ELT section of the ALI Record.  It should begin “PSAP=”.

This section should be populated with the name of the PSAP that should receive the call if the call is able to route correctly.  Example:  PSAP=Coolidge PD.

There are 25 characters available to populate the PSAP name.  This field will use the abbreviations – PD, SO, MO etc.  However, the name of the PSAP/jurisdiction (such as Yuma County) should contain as few abbreviations as possible.  A list of how names should appear in this field can be found further on in this document – titled “PSAP Name Standards”.

Note:  There are 25 characters available to define the PSAP name.  Some Plant (PEI) systems insert an indent or space before the PSAP name.  Therefore, instead of the 26 characters that would otherwise be available, there are only 25.

Note:  Qwest and Intrado have a requirement that the first four characters following “PSAP=” must be unique.  Therefore, there may be a few instances where the name of the PSAP is represented with initials, in addition the full PSAP name.  For instance,

Yuma PD	PSAP=YUPD--Yuma PD

Yuma County SO	PSAP=Yuma County SO

Responsible Party:

The MSAG Coordinator is responsible to pass the PSAP name that populates this field (as defined further on in this document) to Intrado when they secure the wireless ESN(s).

Wireless Service Providers

Name Standards

Below are the wireless service providers, and how their name should appear in the Customer Name Field.

Note:  There are 28 characters available in the Customer Name Field

Company Name	Customer Name Field	# of Characters

Alamosa PCS	Alamosa PCS 866-398-3284	24

Alltel	Alltel 866-820-0429	19

Cellular One of NE AZ	Cellular1 NE AZ 928-532-0082	28

Cingular Wireless	Cingular Blue 800-635-6840	26

Commnet Wireless	Commnet WRLS 720-733-5360	25

Cricket Communications	Cricket 858-882-9301	20

Nextel	Nextel 866-398-3284	19

Sprint PCS	Sprint PCS 866-398-3284	23

T-Mobile USA	T-Mobile USA 973-292-8911	25

Verizon Wireless	Verizon WRLS 800-451-5242	25

PSAP Name Standards

Below are the names of the PSAPs as they should appear in the locality field.  These names will follow “PSAP=”.  There should be no other entries other than shown below.

Note:  There are 25 characters available to define the PSAP name.

Note:  Qwest and Intrado have a requirement that the first four characters following “PSAP=” must be unique.  Therefore, there may be a few instances where the name of the PSAP is represented with initials, in addition the full PSAP name.  For instance,

Yuma PD	PSAP=YUPD-Yuma PD

Yuma County SO	PSAP=Yuma County SO

Wireless 9-1-1 System	Name on ALI Record	# of Characters

PSAP

Coconino County

Coconino SO/Flagstaff PD	Coconino SO Flagstaff PD	24

Dept. of Public Safety	Flagstaff-DPS	13

Grand Canyon National	Grand Canyon Natl Park	22

Park Service

Williams PD	Williams PD	11

Cochise County

Benson PD	Benson PD	9

Bisbee PD	Bisbee PD	9

Cochise SO	Cochise County SO	17

Douglas PD	Douglas PD	10

Fort Huachuca FD	Fort Huachuca FD	16

Huachuca City PD	Huachuca City PD	16

Sierra Vista PD	Sierra Vista PD	15

Willcox PD	Willcox PD	10

Gila County

Gila SO, Globe	GCSO Gila County SO Globe	25

Gila SO, Payson	Gila County SO Payson	21

Wireless 9-1-1 System	Name on ALI Record	# of Characters

PSAP

Globe PD	Globe PD	8

Payson PD	Payson PD	9

Gila River Indian Community

Gila River Indian Comm.	Gila River Indian Commnty	25

Graham County

Graham County SO	Graham County SO	16

Greenlee County

Clifton PD	Clifton PD	10

Greenlee SO	Greenlee County SO	18

Maricopa Region 9-1-1

Apache Junction PD	Apache Junction PD	18

Avondale PD	Avondale PD	11

AZ State University PD	ASU PD	6

Buckeye PD	Buckeye PD	10

Capitol PD	Capitol PD	10

Chandler PD	Chandler PD	11

Dept. of Public Safety	DPS-Phoenix	11

El Mirage PD	El Mirage PD	12

Ft McDowell PD	Ft McDowell PD	14

Gilbert PD	Gilbert PD	10

Glendale PD	Glendale PD	11

Goodyear PD	Goodyear PD	11

Luke Air Force Base	Luke AFB	8

Maricopa County SO	Maricopa County SO	18

Mesa PD	Mesa PD	7

Paradise Valley PD	Paradise Valley PD	18

Peoria PD	Peoria PD	9

Phoenix FD	PFD Phoenix FD	14

Phoenix PD	Phoenix PD	10

Rural Metro FD	Rural Metro FD-Phoenix	22

Salt River Tribal PD	Salt River Tribal PD	20

Scottsdale PD	Scottsdale PD	13

Surprise PD	Surprise PD	11

Tempe PD	Tempe PD	8

Wireless 9-1-1 System	Name on ALI Record	# of Characters

PSAP

Tolleson PD	Tolleson PD	11

Wickenburg PD	Wickenburg PD	13

Mohave County

Bullhead City PD	Bullhead City PD	16

Colorado City PD	Colorado City PD	16

Kingman PD	Kingman PD	10

Lake Havasu City PD	Lake Havasu City PD	19

Mohave County SO	Mohave County SO	16

Page, City of

Glen Canyon National	Glen Canyon Natl Park Svc	25

Park Service

Page PD	Page PD	7

Pima County

Marana PD	Marana PD	9

Oro Valley PD	Oro Valley PD	13

Pima County SD, Ajo	PCSD Pima County SD Ajo	23

Pima County SD, Tucson	Pima County SD Tucson	21

Tucson E911	City of Tucson	14

Pinal County

Casa Grande PD	Casa Grande PD	14

Coolidge PD	Coolidge PD	11

Eloy PD	Eloy PD	7

Florence PD	Florence PD	11

Pinal County SO	Pinal County SO	15

Santa Cruz County

Nogales PD	Nogales PD	10

Santa Cruz County SO	Santa Cruz County SO	20

Winslow, City of

Winslow PD	Winslow PD	10

Winslow FD	WFD-Winslow FD	14

Yavapai County

Camp Verde MO	Camp Verde MO	13

Cottonwood PD	Cottonwood PD	13

Prescott PD	Prescott PD	11

Sedona FD	Sedona FD	9

Sedona PD	SPD-Sedona PD	13

Yavapai SO	Yavapai County SO	17

Wireless 9-1-1 System	Name on ALI Record	# of Characters

PSAP

Yuma County

Somerton PD	Somerton PD	11

Yuma PD	Yuma PD	7

Yuma SO	YCSO-Yuma County SO	19